## Slide 1: ENME480 Lab: Inverse Kinematics
Alex Beyer, Kaustubh Joshi

## Slide 2: Todays Plan
Inverse Kinematics Intro Lecture
Time to work on FK Lab/IK Code

## Slide 3: Announcements
  Exam grades (hopefully) coming out soon, watch for an email telling you how to pick it up and ask for regrades!
  Homework 3 grades hopefully coming shortly after
  Lab group peer reviews are also coming after IK lab finishes
    These will affect your grade!
    Let us know either on Piazza or the peer review if you have a teammate who is not contributing.

## Slide 4: Recap & Motivation
  Forward Kinematics lets us specify and end effector position by giving joint angles
    The joint angles can be highly sensitive to changes in end effector position
    If we want to design a function to move our end effector an inch to the right, how would do that via Forward Kinematics?
    What if we needed to path the end effector around an obstacle? How would a physical object map into joint space? (hint: its usually unintuitive)

## Slide 5: The Inverse Kinematic Problem
  Given a robot with a desired end effector position p (and potentially orientation φ) and set of constraints f, solve for a set of joint states s which will move the end effector to the desired position, subject to the constraints.
  (we’ll leave dealing with constraints for another time!)
What kind of problem are we doing here?

## Slide 6: Issues
  Imagine using your hand to pick up a block – is there only one valid way to bend your arm?
    There are (in general) multiple solutions via IK for most points
Theres 2 for this robot, but how does this scale?

## Slide 7: Issues
  Outside a very particular set of systems (or set of constraints) we’re going to end up with an indeterminant system
  No matter how we work this system we will not find a closed form solution without making major assumptions about how the robot moves!
  Need to solve numerically!

## Slide 8: Solving the IK Problem - Cases
  CASE I: An Analytical Solution Exists
    Number of system DoF is low enough (or your assumptions are specific enough) to enable you to find a closed for equation of the form:
    Rare this will happen
    Requires robots/poses built in special ways
    Just solve the equation
      (easy-ish to solve so we gave you one for the project)
Notes: Think analytic vs numeric!!!

## Slide 9: Solving the IK Problem - Cases
  CASE I: An Analytical Solution Exists
    Example: Given solve for
Notes: Think analytic vs numeric!!!

## Slide 10: Solving the IK Problem - Cases
  CASE I: An Analytical Solution Exists
    Example: Given solve for
Bent elbow  two solutions to IK
What do we do?
Pick one and use it as a constraint!
Notes: Think analytic vs numeric!!!

## Slide 11: Solving the IK Problem - Cases
  CASE I: An Analytical Solution Exists
    Example: Given solve for
This gives the elbow up angle, we could also say:
And recover both solutions.
Then:
Notes: Think analytic vs numeric!!!

## Slide 12: Solving the IK Problem - Cases
  CASE 2: Most of An Analytical Solution Exists
    The most common problem
    How this is usually done in the real world
    Combines techniques from the prior two cases
    Interesting!
    Results in us having to solve a highly nonlinear function numerically
      Cyclic Coordinate Descent (CCD)
Notes: Coordinate descent (along with its many, many variants) is the most common approach

## Slide 13: Solving the IK Problem - Cases
  CASE 2: Most of An Analytical Solution Exists
Globally Optimal Inverse Kinematics as a Non-Convex Quadratically Constrained Quadratic Program,
Tomáš Votroubek and Tomáš Kroupa
Notes: Coordinate descent (along with its many, many variants) is the most common approach

## Slide 14: Solving the IK Problem - Cases
  CASE 3: Most of An Analytical Solution Exists
Globally Optimal Inverse Kinematics as a Non-Convex Quadratically Constrained Quadratic Program,
Tomáš Votroubek and Tomáš Kroupa
Notes: Coordinate descent (along with its many, many variants) is the most common approach

## Slide 15: Solving the IK Problem - Cases
  CASE 3: An Analytical Solution Does Not Exist
    More common
    Lack of assumptions makes it hard to say much
    Results in us having to solve a highly nonlinear function numerically
      Gradient Descent (GD)
Notes: Coordinate descent (along with its many, many variants) is the most common approach

## Slide 16: Numerical Methods
  This is the barest bones version of the basics!
  Instead of solving a large, complex equation outright break it into smaller, easier to solve steps and add those together!
    Lowering the per step error  Lowering the overall error
  If you’ve ever used FEA Software (CAD) or an integrator in Python/MATLAB (ode45) this is what you’ve been doing!
  Think of Riemann Integration

## Slide 17: Implementation
  Instead of thinking about the problem as “drive my end effector to a given position” let’s think about it as “how far away is my end effector from the final position?”
    This is now an optimization problem
  This is easier to optimize now, but we still don’t have a clear function to solve to get zero error
    What should our next step be?

## Slide 18: Implementation - Approach
  Start with an initial guess for the state si and calculate its error
  Generate another guess, offset by some amount and calculate its error
    Think back to Calc 1, what can we say about optimality by doing this?
  Use this to inform your next guess and check again
    Remember to use your constraints to inform your next guess(es), they can narrow down the number of valid next guesses
  Repeat this process until your error is below a threshold value

## Slide 19: Implementation - Structure
  Now we have a clearer understanding of our problem, but how do we find the error?
    Forward Kinematics!
A guess for the robot angles which will inform…
An estimate for the cartesian end effector which position will inform…

## Slide 20: Implementation - Issues
  Forward Kinematics have the advantage of always working for a valid set of angles; not all valid points will work nicely in IK
    Multiple sets of angles can correspond to one point, how do we pick?
  Some singularities are purely mathematical; the math might say you’re stuck in a certain pose and can’t move but physically there’s nothing stopping you

## Slide 21: Implementation
We mentioned how moving in joint space is difficult, let’s revisit this concept: (desired point: <3,2>)
Notes: Y=mx+b (technically affine)  solve for 0  we’re finding this proportionality relationship btwn y and x then using it to backsolve in one step
This does not work for nonlinear systems

## Slide 22: Descent Methods – Background
Potential Problems:
  Motions in joint space aren’t clearly mapped to cartesian space
  Local (but not global) minima
    This 2 DoF planar case doesn’t have any, but higher DoF cases would
  By extension, we are extremely sensitive to ICs
  Need to calculate rate of change for a function we might not know
    Numerical Derivatives
      Stationary points
    Added complexity  higher chance for the math to break down
Notes: Think analytic vs numeric!!!

## Slide 23: Descent Methods – Method
For end effector position p and joint state θ (both vectors):
Pick an initial condition
Set a desired precision and repeat:
  Calculate dp/dθ
  Pick a direction (randomly or otherwise)
  Update your guess according to:
  Update error, break if you’ve reached your desired precision
Notes: Think analytic vs numeric!!!

## Slide 24: Descent Methods – Jacobians
With respect to n variables
The derivative of m states
Two problems when finding dp/dθ
  First: Matrix Derivatives
  What is the Jacobian telling you? What can we use this information for?
Yields an m by n Jacobian
Notes: Think analytic vs numeric!!!

## Slide 25: Descent Methods – Jacobians
Two problems when finding dp/dθ
  Second: (Forward) Finite Differencing
    We don’t have an analytical function to take a derivative, need to approximate
    (this is the numerical methods part)
This is the central argument for all numerical derivatives and integrals
Notes: Think analytic vs numeric!!!

## Slide 26: Breaking Descent Methods
To understand how the method works, we also need to understand why it doesn’t
Think back to the list of issues before, which ones will we still face?
Notes: Think analytic vs numeric!!!

## Slide 27: Breaking Descent Methods
To understand how the method works, we also need to understand why it doesn’t
Think back to the list of issues before, which ones will we still face?
  Sensitivity to ICs – fundamental to the method
  Local Minima – also fundamental to the method
  Stationary Points – we can design corrections for this
  IK Singularities – needs investigating
Notes: Think analytic vs numeric!!!

## Slide 28: Breaking Descent Methods – Stationary Points
  Stationary points in the error function behave like valid solutions (locally) with high error
  How do we fix?
    Perturb our guess for θ by Δθ in all directions, increasing the magnitude of Δθ if we fall back to the same point
  This thought process broadly applies to local minima as well
Notes: Think analytic vs numeric!!!

## Slide 29: Breaking Descent Methods– Identifying Singularities
Two main types of singularity:
  Boundary Singularities
    Occur when hyperextending a joint, determined by the physical structure of the robot
  Internal Singularities
    Purely mathematical, typically caused by the joint axes aligning during a movement
    Result in either an infinite number of solutions (we need some choice criteria) or result in math that, when worked out, requires infinite joint velocity/force
    Ex: two axes aligning such that the motion in one perfectly cancels the motion in the other
Notes: Solution space loses dimensions for internal singularities; equivalent to no longer having a unique solution to things
We can spot this via the Jacobian, but I’ll leave that for a later class that can spend multiple lectures building this idea (its incredibly powerful and I don’ want to misspeak)

## Slide 30: Solving the IK Problem - Cases
  These are not 3 unrelated methods; they share a lot of techniques and approaches
  Think of it as a spectrum from fully numeric to fully analytic
Heuristic Methods
Analytic Methods
Numeric Methods
Notes: Coordinate descent (along with its many, many variants) is the most common approach

## Slide 31: Assignment Code - Structure
  Download the lab4_scripts.zip file from Canvas
    Only edit the lab4_func.py file!
  Copy and paste your working Lab 3 code into lab4_func.py in the designated space, you’ll use this to verify your guesses
  We’ve given you a skeleton outline for what order you should find things in

## Slide 32: Assignment Code - Constraints
  The UR3e robot is a 6 DoF robot meaning we need to solve for 6 configuration variables
  We added the constraint that we want joint 5 (the 2nd wrist joint) to always be –π/2, pointing straight down
    Now we’re down to 5 DoF
  Additionally, we’re passing in a desired yaw value
    No reduction in DoF, but we do get another equation to use (4 variables in 5 equations)
  Finally, we specify the “elbow up” configuration
    This doesn’t become an equation, but it does give us a rule to discard solutions

## Slide 33: Final Notes
FK Lab due Friday!
  UR3e DH table posted to the wiki
IK lab due in 2 weeks

## Slide 34
Notes: Solution space loses dimensions for internal singularities; equivalent to no longer having a unique solution to things
We can spot this via the Jacobian, but I’ll leave that for a later class that can spend multiple lectures building this idea (its incredibly powerful and I don’ want to misspeak)

## Slide 35: Notes on DH Parameters
  Any transform (Ti-1i, for example) is made of four operations:
    Offset a distance di along zi-1 to the common normal of frames {i-1} and {i}
      If no common normal exists, pick a convenient value for di
    Rotate xi-1 by θi to align it with xi
    Translate a distance ai along the common normal, from xi-1 to xi
    Finally, rotate by an angle αi about xi to align zi
Frame {i-1}
Frame {i}
Joint {i}
Joint {i+1}

## Slide 36: Notes on DH Parameters
  There are pointers for how to align your axes to make this easier:
    The xn axis must intersect and be perpendicular to zn and zn-1
    The origin of the nth joint lies at the intersection of xn and zn
    yn is any valid axis that completes a right handed frame
      Remember the right hand rule when finding angles!
Frame {i-1}
Frame {i}
Joint {i}
Joint {i+1}

## Slide 37: Motivation
  In the process of doing Forward Kinematics we derived a set of equations for our geometry as a function of our DoFs
  We know that we have some workspace in cartesian space where the end effector can reach
  Trying to navigate joint space to move around the workspace is unintuitive and confusing (what does a unit change in a joint angle do to the end effector?)
  What if we want to find joint angles corresponding to an end effector position?

## Slide 38: Motivation
  Approaches based in FK are fundamentally limited, but give a useful set of equations from the geometry:
  What if we ran these equations in reverse?
Can you see the problem?